## Slide 1
Fig. 1 Location of sampling sites
Ambient air samples were collected once a month for five years (from 2005 to 2009) at six sites which comprehend urban areas (Sanda, Nishiwaki, Toyooka, and Sumoto), a roadside area (Ashiya), and an industrial area (Takasago) in Hyogo Prefecture, Japan.

## Slide 2
Fig. 2 Health risk estimation for VOCs by excess cancer incidence
The target compounds of health risk estimation by excess cancer incidence are 10 VOCs which the unit risk values are established by U.S. EPA. The vertical axis are shown as logarithmic scale. For formaldehyde, acrylonitrile, and acetaldehyde, the excess cancer incidences were more than 10-5 of the level of concern for carcinogenic effect at one or more sites. Particularly, in formaldehyde, they were in the 10-4 to 10-5 range at all sites.

## Slide 3
Fig. 3 Health risk estimation for VOCs by hazard quotient
The target compounds of health risk estimation by hazard quotient are 26 VOCs which the reference concentration values are established by U.S. EPA etc.. The vertical axis are shown as logarithmic scale. Although the hazard quotients of acrylonitrile, 1,3-butadiene, acetaldehyde, and toluene were higher than those of other substances, they were less than 1 of the level of concern for noncarcinogenic effect at all sites.

## Slide 4
Fig. 4 Ozone production for VOCs at sampling sites
The individual ozone productions of 87 VOCs except toluene, 1-butene, m-,p-xylene, formaldehyde, acetaldehyde, ethylbenzene, and 1,2,4-trimethylbenzene were low respectively. Thus, for 87 VOCs, the total amount of each ozone production was indicated. At all sites, toluene had a high percentage of the ozone production.

## Slide 5
Fig. 5 The trends of the annual mean concentrations for toluene at sampling sites
The interannual change tendencies of toluene concentrations were different at a regional level. It was determined that the annual mean concentrations generally continued to be flat in Nishiwaki, Toyooka, Sumoto, and Ashiya, and exhibited an increasing tendency in Sanda. And, in Takasago, the annual mean concentration in 2007 was relatively higher than others.

## Slide 6
Concentration (mg/m3)
Fig. 6 The trends of the seasonal concentrations for toluene at sampling sites (median)

## Slide 7
Fig. 7 The trends of the annual mean concentrations for formaldehyde at sampling sites
Formaldehyde concentrations have been reduced at all sites in 2009 compared to the previous year. Especially, in Ashiya, it exhibited relatively more reduction rate than others.

## Slide 8
Concentration (mg/m3)
Fig. 8 The trends of the seasonal concentrations for formaldehyde at sampling sites (median)
The seasonal concentrations increased from spring to summer and decreased from summer to winter at all the urban sites. There were significant differences between formaldehyde concentrations in summer and winter at above sites except Ashioya as roadside area (1% significance, Wilcoxon test).