## Slide 1
Rapid Screening for Synthetic Antidiabetic Drug Adulteration in Herbal Dietary
Supplements Using Direct Analysis in Real Time Mass Spectrometry
Zhigui Zhou, Jialing Zhang, Wei Zhang, Yu Bai* and Huwei Liu
Institute of Analytical Chemistry, College of Chemistry and Molecular Engineering, Peking University, Beijing 100871, China.
E-mail: yu.bai@pku.edu.cn
Overview
Introduction
Methods
Results
 | Methanol/water (1:1, v/v) ng/mL | Matrix 1 ng/mL (μg/g*) | Matrix 2 ng/mL (μg/g*) | Matrix 3 ng/mL (μg/g*)
Metformin | 100 | 200 （20） | 400 （40） | 800 （80）
Nateglinide | 100 | 200 （20） | 200 （20） | 400 （40）
Gliclazide | 20 | 20 （2） | 40 （4） | 80 （8）
Rosiglitazone | 20 | 40 （4） | 40 （4） | 40 （4）
Glipizide | 500 | 2000 （200） | 2000 （200） | 30000 （3000）
Glibenclamide | 1000 | 1000 （100） | 1000 （100） | 2000 （200）
Gliquidone | 200 | 400 （40） | 1000 （100） | 4000 （400）
Instruments
DART®-SVP source (IonSense, MA, U.S.A.)
Agilent 6530 Accurate-Mass Quadrupole Time-of-Flight mass spectrometer (Agilent Technologies, CA, U.S.A.)
Sample preparation and detection
100 mg of herbal dietary supplement added to 10 mL of methanol/water (1:1, v/v);
Shake manually for several seconds;
A tip dipped into the extract for 5 seconds;
Position the tip in the helium stream of the DART source for 10 seconds to acquire the MS or MS/MS data.
Adulteration of synthetic antidiabetic drugs in herbal supplements without labeling is illegal, which puts diabetic patients or elderly people taking a large amount of adulterated supplements in great danger of adverse effects of synthetic drugs. Thus rapid, sensitive and reliable methods are required for adulterant screening. In this work, a rapid and reliable method was developed for the screening of seven synthetic antidiabetic drugs adulterated in herbal dietary supplements using DART-QTOF MS, and only several minutes in total were required for the examination of each herbal dietary supplement.
Adulterant screening by using DART-QTOF MS
Manually shaking one-step sample pretreatment
Adulteration confirmation by combination of accurate m/z
values and MS/MS data
Examination of commercial herbal dietary supplements
Optimization of DART operating conditions
Fig. 1 The optimization of DART parameters affecting the detection sensitivities of seven synthetic drugs. a-g: helium gas temperature (n=6), h-n: gas flow rate (n=3).
Fig. 2 MS/MS spectra of the seven synthetic drugs together with the proposed fragmentation pathways.
Optimization of collision energies for MS/MS
The collision energies were optimized so that at least three characteristic fragments labeled in Fig.2 with stable relative abundance were selected in our experiments for the confirmation of the adulteration.
LODs in methanol/water and herbal supplement matrices
* The LODs of synthetic drugs in the capsules or tablets of herbal dietary supplements (shown in the brackets) were calculated according to the corresponding spiked concentrations in supplement extracts.
Fig.3 MS and MS/MS spectra of the two herbal dietary supplements adulterated with metformin. a, d: EICs (m/z 130.11) of three repeated sample introduction, b, e: MS spectra with background subtracted, c, f: MS/MS spectra of m/z 130.11.
This work was supported by the National Natural Science Foundation of China (Grant No. 21027012, 90717002 and 20975005) and the fundamental research funds for the central universities.
Conclusion
The LOD values, ranging from 2 to 400 μg g-1 (except for 3 mg g-1 of glipizide in matrix 3), could satisfy the requirements for detecting adulterant antidiabetic drugs (usually added at the level of several hundreds of micrograms to several milligrams per gram to obtain the antidiabetic effect).
Five herbal supplement products were tested, and two were adulterated with metformin.