## Slide 1
MESURMENT OF ACCUMULATION OF HYDROXYLATED POLYCHLORINATED BIPHENYL (OH-PCBs)
IN HUMAN URINE AND BLOOD
Nobutake Sato1, Jun Yonekubo1, Tatsuya Ezaki1, Motoharu Suzuki2, Chisato Matsumura3, Yuki Haga3, Takeshi Nakano3,4
1Nihon Waters K.K, 2Kobe University, Graduate School of Agricultural Science, 3Hyogo Prefectural Institute of Environmental Sciences, 4Osaka University, Center for Advanced Science and Innovation,
Polychlorinated biphenyls (PCBs) are known as environmental contaminants that may cause abnormal effect in various organs and some studies determined the residue levels and patterns of PCBs and metabolized PCBs (hydroxylated PCB : OH–PCBs) congeners in human blood. Hydroxyl group of OH-PCBs has high acidity, therefore OH-PCBs was made metoxy-derivatization and analyzed with GC-HRMS. Complicated preparations are needed for analyzing with GC-HRMS, beside that identifying methoxy metabolized PCBs and methoxy-derivatization OH-PCBs is difficult.
Our previous study determined elution order for 51 congeners of OH-PCB without derivatization and developed an analytical method for quantity to separate mixture of 6 major OH-PCBs in human blood (4'-OH-CB-107, 3-OH-CB-138, 4’-OH-CB-146, 3-OH-CB-153, 4’-OH-CB-172 and 4-OH-CB-187) and 4'-OH-CB-165 which is difficult to be separated from 3-OH-CB-153 with GC-HRMS, then applied analytical method to biological sample of human urine with UPLC/QTof MS.
The present study aimed at measuring of OH-PCBs in human urine and blood sample taken from same person , evaluating accumulation of each OH-PCB isomer and congener and comprehending dominant metabolized PCBs in each human urine and blood.
Figure 2. Sample preparation of urine sample
INTRODUCTION
RESULTS AND DISCUSSION
Table 1. Concentration of OH-PCBs in serum and urine.
(serum analyzed whit GC/MS, urine analyzed whit LC/MS)
METHODS
References
1.Suzuki M., Okuno T., Matsumura C., Sato N., Yonekubo J., Ezaki T., Inoue Y., Imaishi H., Nakano T., 2011 Development of
hydroxylated polychlorinated biphenyl(OH-PCB) analytical method in human urine with UPLC/Q-Tof MS. Dioxin 2011
2.Ezaki T., Yonekubo J., Suzuki M., MatsumuraC., Nakano T., 2010 Development of low level hydroxyllated polychlorinated
biphenyl(OH-PCBs) analytical method in human blood with UPLC/Q-Tof MS. Dioxin 2010
3.Kuroki H., Haraguchi K., Saito H., Masuda Y., Wehler EK., Bergman A., 1993 Accumulation of hydroxylated PCB metabolites
in blood. Fukuoka Igaku Zasshi. May;84(5), 248-56
4.Britta F., Maria A., Philippe G., Pal W., Ake B., 2002. Hydroxylated PCB Metabolites and PCBs in Serum from Pregnant
Faroese Women. Environmental Health Perspectives Vol. 110
OH-PCBs Standard Solution:
Six major compounds standard solution of OH-PCBs in human blood and 4'-OH-CB-165 (see Fig.1) were purchased from Wellington Laboratories Inc. (Guelph,ON, Canada) and each solution was diluted in acetone.
Figure 1. Structure of major 6 OH-PCBs and 4’-OH-CB 165
Sample preparation of urine:
Urine(100～200 mL)
Add X1, 20mM Phosphate buffer (pH 4.0).Add IS
Extraction
2 mL of CH2Cl2 X 2 times
Adjust pH at 4.0 with
10%-HCOOH aq.
Solid Phase Extraction
(RP-WAX:240 mg)
Elute with 8 mL
of 0.1%-NH3 in methanol
Concentration
Less than 1 mL by N2 gas
Add. 5mL of 20mM-
Phosphate buffer (pH 7.0 )
Add. 20 μL β-Glucuronidase
/ Aryl sulfatase,
Enzyme reaction
at 37 degree for 1.5 hr
Centrifugation
2600 rpm. for 10 min
Concentration
1 mL by N2 gas
Concentration
1 mL by N2 gas
Add. X 9 CH3CN
LC/MS analysis
Analytical condition:
Seven OH-PCBs can be separated in this analytical condition of LC. High resolution MS (TOF MS)was used for detection of each congener.
UPLC |  |  | 
Instrument: | ACQUITY UPLC |  | 
Column: | BEH C18 2.1ID X 150 mm, 1.7um |  | 
Flow rate: | 0.5 mL/min. |  | 
Column heater: | 60 degree celsius |  | 
Mobile Phese A: | 5mM CH3COONH4 aq. |  | 
Mobile Phese B: | THF/CH3CN (v/v: 1/4) |  | 
Gradient : |  |  | 
Time(min) | %A | %B | 
0.0 | 75 | 25 | 
17.0 | 25 | 75 | 
18.0 | 1 | 99 | 
18.5 | 75 | 25 | 
Total Run Time: | 20 min |  | 
MS | 
Instrument: | Xevo G2 Q-TOF
Ionization mode: | ESI negative
Capillary: | 1.5 kV
Sampling Cone: | 40 V
Source Temp: | 120 degree celsius
Desolvation Temp: | 600 degree celsius
Cone Gas Flow: | 20 L/hr.
Desolvation Gas Flow: | 800 L/hr.
Resolving Power: | <22,500
Selected Ion: | 
Penta-chloro/OH-CB | m/z=340.8675
Hexa-chloro/OH-CB | m/z=374.8286
Hepta-chloro/OH-CB | m/z=408.7896
Sampling | Concentration in serum(pg/g serum) |  |  |  |  | 
(year/date) | 4-OH-107 | 3'-OH-138 | 3-OH-153/4-OH-146 |  | 4-OH-172 | 4-OH-187
2011/0814 | 307 | 102 | 617 |  | 62 | 155
2012/0428 | 52 | 24 | 105 |  | 25 | 58
2012/0623 | 177 | ND | 289 |  | ND | 122
Sampling | Concentration in urine(pg/mL urine) |  |  |  |  | 
(year/date/time) | 4-OH-107 | 3'-OH-138 | 3-OH-153 | 4-OH-146 | 4-OH-172 | 4-OH-187
2012/0623/2330 | N.D | N.D | N.D | N.D | N.D | N.D
2012/0624/0220 | N.D | 1.10 | 0.48 | N.D | N.D | N.D
2012/0624/0410 | 0.55 | N.D | N.D | N.D | N.D | N.D
2012/0624/0645 | 0.47 | 0.74 | 0.19 | N.D | N.D | N.D
2012/0624/0900 | 0.42 | 1.29 | 0.21 | N.D | N.D | N.D
2012/0624/1120 | 0.74 | 1.95 | 0.47 | N.D | N.D | N.D
2012/0624/1800 | 2.00 | 3.13 | 2.00 | N.D | N.D | N.D
2012/0624/2120 | 1.24 | 3.05 | 1.81 | N.D | N.D | N.D
4-OH-CB-107
3'-OH CB-138
3-OH CB-153
Figure 2. Chromatogram of detected OH-PCBs in urine
Conc. in urine(pg/mL)
Conc. in serum(pg/g)
Chart: 
| 4-OH-107 | 3'-OH-138 | 3-OH-153(OH-153/146) | 4-OH-187
urine2330 | 0 | 0 | 0 | 0
urine0220 | 0 | 1.0952 | 0.47619 | 0
urine0410 | 0.55 | 0 | 0 | 0
urine0645 | 0.46512 | 0.74419 | 0.18605 | 0
urine0900 | 0.41667 | 1.2917 | 0.20833 | 0
urine1120 | 0.73684 | 1.9474 | 0.47368 | 0
urine1800 | 2 | 3.1304 | 2 | 0
urine2120 | 1.2381 | 3.0476 | 1.8095 | 0
serum0623 | 177 | 0 | 289 | 122
Figure 3. Time course of OH-PCBs concentration in urine
comparing to serum taken from same person
Main detected OH-PCBs in blood was 4-OH-107, 3-OH-153/4-OH-146 and 4-OH-187, on the other that in urine was 4-OH-107, 3’-OH-138 and 3-OH-153, pattern of detected compound is different from each sample(see Table 1 and Fig.3).Time course of concentrations of OH-PCBs in urine in a day, there is tendency that all detected compounds increase not only specific OH-PCB.
These might indicate that each isomer and congener has characteristic to metabolic and transport pathway into serum and urine individually and pattern of detected OH-PCBs is different between blood and urine.